Appendix A1

A1.1 Programul principal de rulare si prelucrare primara a datelor (folosind modelul SimuLink)

| 1 | %se ruleaza "LD_ DinExterior.mdl" de Nr+1 ori, si la fiecare frecventa in |
| --- | --- |
| 2 | %intervalul FrecvOmega=OmIn:dOmegaFaza:OmOut se calculeaza sigma (din statistica raportului de faze)... |
| 3 | %trebuie setat aici Nr, OmIn, OmOut si in mdl "Durata simulare" (initial 1e6) |
| 4 |  |
| 5 | clear all;clc |
| 6 | %global PmfPh PmfPhD m_n DDt FREq t_PmfPhD FiPM FiOmega pOm pPM X NN Xii pdf_H sigma_HIST Smax S1 nxh n1 |
| 7 | global X NN Xii pdf_H sigma_HIST Smax S1 nxh n1 |
| 8 |  |
| 9 | c = clock;fisier=['date.' num2str(c(5)) num2str(c(6)) '.dat']; |
| 10 | fid = fopen(fisier,'w'); % open a file to write data |
| 11 |  |
| 12 | %%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%DATE INITIALE |
| 13 | TimpSimulare=[0 1e-8]; %timpul unei simulari din cele scanate... |
| 14 | I=[0 15e-3]; |
| 15 | %ca sa avem traiectoriile modurilor diferite trebuie sa avem d_om_g_==e12! si fara ()^2 !!!!! in ec. dN/dt !!! |
| 16 |  |
| 17 | OmIn=0; %frecventa initiala EOM |
| 18 | OmInI=0;%0.1e9;%1.97E9; %frecventa initiala Curent |
| 19 | dOmegaFaza=1e8; %5e7;2e7 |
| 20 | NrOmega=1; %numarul de frecvente scanate |
| 21 |  |
| 22 | AIn=0;%0.02; %amplitudinea initiala |
| 23 | dAmod=0.02; %.1 |
| 24 | NrAmp=1; %numarul de amplitudini scanate |
| 25 |  |
| 26 | OmOut=OmIn + (NrOmega-1)*dOmegaFaza; |
| 27 | OmOutI=OmInI + (NrOmega-1)*dOmegaFaza; |
| 28 | AOut=AIn + (NrAmp-1)*dAmod; |
| 29 | %%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%5 |
| 30 |  |
| 31 | for kk=1:NrAmp |
| 32 | for k=1:NrOmega |
| 33 | tic; |
| 34 | FileName=[num2str(kk) '_' num2str(k)]; |
| 35 |  |
| 36 | %OmegaFaza=[0 OmIn+(k-1)*dOmegaFaza]; |
| 37 | %Amod=[0 AIn+(kk-1)*dAmod]; |
| 38 | OmegaFaza=[0 0]; |
| 39 | Amod=[0 0]; |
| 40 |  |
| 41 | OmegaFazaI=[0 OmInI+(k-1)*dOmegaFaza]; |
| 42 | AmodI=[0 AIn+(kk-1)*dAmod]; |
| 43 | %OmegaFazaI=[0 1.92e9]; AmodI=[0 0.34] |
| 44 |  |
| 45 | tic |
| 46 | %[OmegaFaza(2) Amod(2) OmegaFazaI(2) AmodI(2) I] |
| 47 | %sim('A_LD_DinExterior.mdl'); |
| 48 | sim('LD_Matlab7.mdl'); |
| 49 | toc |
| 50 |  |
| 51 | plot(t,Pm) |
| 52 | aaa %stop... |
| 53 |  |
| 54 | %%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%% |
| 55 | N=size(t,1); |
| 56 | Nini=1000; Nfin=Nini; t=t(Nini:N); Pmf=Pmf((Nini:N)); %t=t(1:Nfin); Pmf=Pmf((1:Nfin)); |
| 57 | N=size(t,1); |
| 58 | %plot(t,Pmf); print -dmeta FileName; movefile('FileName.emf',[FileName '.emf']) |
| 59 | %h=figure; hgsave(h,[num2str(kk) '_' num2str(k)] ) |
| 60 |  |
| 61 | %---------------------------------- |
| 62 | %[t_PmfPhD,FiPM,FiOmegaInt]=PhaseRect(t,Pmf,N,OmegaFaza(2)); |
| 63 | [t_PmfPhD,FiPM,FiOmegaInt,n_m]=PhaseRect(t,Pmf,N,OmegaFazaI(2)); |
| 64 | movefile('FileName.emf',[FileName '.emf']) |
| 65 | NN=size(t_PmfPhD,1); |
| 66 |  |
| 67 | if NN>2 %numarul de caderi in LFF |
| 68 | [rap]=PhaseDiff(t_PmfPhD,FiPM,FiOmegaInt); %raportul fazelor... |
| 69 | [r_frq,r_faze]=RapFreq(t_PmfPhD,FiPM,FiOmegaInt); %raportul frecventelor |
| 70 | sigma_HIST=StatHist(r_frq,diff(t_PmfPhD)); %statistica HIST |
| 71 | %figure;plot(t_PmfPhD,r_faze);title('R\phi_{\it12}') |
| 72 | else |
| 73 | rap=NaN; |
| 74 | sigma_HIST=NaN; |
| 75 | end |
| 76 | %%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%% |
| 77 |  |
| 78 | %!!! FrecvOmega(k+1)=OmegaFaza(2); |
| 79 | %!!! Amodulatie(k+1)=Amod(2); |
| 80 | FrecvOmega(kk,k)=OmegaFazaI(2); |
| 81 | Amodulatie(kk,k)=AmodI(2); |
| 82 | RaportFaze(kk,k)=rap; |
| 83 | sigma(kk,k)=sigma_HIST; |
| 84 | Nrcaderi(kk,k)=NN; |
| 85 |  |
| 86 | FRQQ=2*pi*OmegaFazaI(2)/rap; |
| 87 | rapp(kk,k)=n_m; %raportul frecventelor din PhaseRect |
| 88 | FRQ_=2*pi*OmegaFazaI(2)/n_m; %frecventa medie din PhaseRect |
| 89 |  |
| 90 | k |
| 91 | fprintf(fid, '%6.15e %6.15e %6.15e %6.15e\n %6.15e\n',FrecvOmega(kk,k), sigma(kk,k), Amodulatie(kk,k), RaportFaze(kk,k), Nrcaderi(kk,k)); %write in file |
| 92 | save date FrecvOmega sigma Amodulatie RaportFaze Nrcaderi rapp; |
| 93 | clear t Pm Pmf |
| 94 | toc |
| 95 | end |
| 96 | end |
| 97 |  |
| 98 | fclose(fid); %close file |
| 99 | save date FrecvOmega sigma Amodulatie RaportFaze Nrcaderi; |
| 100 |  |
| 101 | %clear; load date_Frecv_Sigma; figure;plot(FrecvOmega,sigma) |

A1.2  Programul principal (folosind integrarea directa Runge-Kutta cu pas fix)

| 1 | clear all; format long |
| --- | --- |
| 2 | global alfa g n0 taun taup s gama beta I e tau omga Omgeom modl Eret |
| 3 |  |
| 4 | g = 1.5e4; n0= 1.5e8; gama = 5e10; taun = 2e-9; taup = 2e-12; |
| 5 | alfa = 5; s = 5e-7; beta = 1.1e3; feom =1e9; Omgeom=2*pi*feom; |
| 6 | e=1.6e-19; omga=1.2e15; |
| 7 | I = 18e-3; |
| 8 |  |
| 9 | y = [1 2e8]'; %y(1)== E // y(2)== n |
| 10 |  |
| 11 | N=10000; h=3e-12; %dt (picosecunde) |
| 12 | tau=100e-12; %timpul de zbor in cavitate |
| 13 | delay=round(tau/h); %intarzierea in cavitate |
| 14 | FunFcn= FuncInteg; %functia de integrat |
| 15 | %fid = fopen('laser1.dat','w'); |
| 16 |  |
| 17 | %Runge-Kutta |
| 18 | for index=1:1:N |
| 19 | modl=pi*sin(Omgeom*index*h); |
| 20 | Efield(index) = y(1); %intarzierea |
| 21 | if index>delay |
| 22 | Eret = Efield(index-delay); |
| 23 | else |
| 24 | Eret =0; |
| 25 | end |
| 26 | K1 = h*feval(FunFcn, index, y); |
| 27 | K2 = h*feval(FunFcn, index+1/2, y+K1/2); |
| 28 | K3 = h*feval(FunFcn, index+1/2, y+K2/2); |
| 29 | K4 = h*feval(FunFcn, index+1, y+K3); |
| 30 |  |
| 31 | y = y + (K1 + 2*K2 + 2*K3 + K4)/6; |
| 32 | %fprintf(fid, '%3.21f\n',abs(y(1))); |
| 33 |  |
| 34 | end |
| 35 | %fclose(fid); |
| 36 |  |
| 37 | time=[1:N]*(h/1e-9); |
| 38 | subplot(2,1,1); plot(time,abs(Efield)); title('Semiconductor Laser Chaos '); |
| 39 | xlabel('Time (ns)','fontsize',10); ylabel('Electric Field (a.u.)','fontsize',10); |
| 40 | set(gca,'fontsize',8,'XColor','black','YColor','black'); axis([1 30 0 500 ]) |
| 41 |  |
| 42 | FX = fft(abs(Efield),N); PXc = FX.*conj(FX)/N; %spectrul de putere |
| 43 | fc = (1/h)*(0:(N/2-1))/N; %esantionarea h |
| 44 | Pc=Log10(PXc); |
| 45 |  |
| 46 | subplot(2,1,2); plot(fc,Pc(1:N/2),'k'); title('RF Power Spectrum of the laser field E '); |
| 47 | xlabel('Frequency(Hz)','fontsize',10); ylabel('Log(Power)','fontsize',10); |
| 48 | set(gca,'fontsize',8,'XColor','black','YColor','black'); axis([0 10e10 -3 8]) |

FuncInt

| 1 | function ydot=FuncInteg(index,y) |
| --- | --- |
| 2 | global alfa g n0 taun taup s gama beta I e tau omga Omgeom modl Eret |
| 3 |  |
| 4 | F=[.5*(1-j*alfa)*(g*(y(2)-n0)/(1+s*abs(y(1)^2))-1/taup)*y(1)+gama*Eret*exp(j*omga*tau)*modl/1000; |
| 5 | I/e-y(2)/taun-(g*(y(2)-n0)/(1+s*abs(y(1)^2)))*abs(y(1))^2 ]; |
| 6 |  |
| 7 | ydot= F; |
| 8 | end |

A1.3 Rutinele programului A1.1

PhaseRect

| 1 | function [t_PmfPhD,FiPM,FiOmegaInt,n_m]=PhaseRect(t,Pmf,N,Omega) |
| --- | --- |
| 2 |  |
| 3 | %-------------------------ATENTIE se alege CUT_N si CUT_P... corespunzator! |
| 4 | CUT_P=7; %ATENTIE de la Max(Pmf)/4 incepe taierea pentru determinarea caderilor |
| 5 |  |
| 6 | PmfM=max(Pmf);Pmfm=min(Pmf);PmfMean=mean(Pmf);Pcut=1*(PmfM-Pmfm)/CUT_P; %Pcut puterea de la care consideram cadere |
| 7 | PmfPh=sign(Pmf-Pcut); %semnalul dreptunghiular asociat, cazul caderilor de putere "aleatoare" |
| 8 | %PmfPh=sign(Pmf-PmfMean); %pentru cazul oscilatiilor "sinusoidale" |
| 9 |  |
| 10 | %PmfPh=sign(Pmf-1.4e-4); |
| 11 | %figure;plot(t,PmfPh*PmfM,t,Pmf); |
| 12 | PmfPhD=fix(diff(PmfPh)/2+0.2);PmfPhD(N)=0; %functii delta la pozitiile de urcare ale semnalului |
| 13 |  |
| 14 | CUT_N=floor(N/20); %de la ce indice temporar se ia in considerare semnalul |
| 15 |  |
| 16 | DDt=t(N)-t(CUT_N); %de unde incep caderile... |
| 17 | FREq=sum(PmfPhD(CUT_N:N))/DDt; %frecventa medie a semnalului... |
| 18 | Freq=FREq*2*pi; |
| 19 | n_m=Omega/FREq; |
| 20 | %NrTotalCaderi=sum(PmfPhD); %DIN INTERVALUL DDt !!! |
| 21 |  |
| 22 | t_PmfPhD=nonzeros(PmfPhD.*t); %timpul corespunzator la pozitiile de urcare ale semnalului |
| 23 | FiPM=cumsum(nonzeros(PmfPhD))*2*pi; %faza "caderilor" in punctele de urcare |
| 24 | %figure;plot(t_PmfPhD,FiPM) %variatia fezei caderilor |
| 25 |  |
| 26 | FiOmega=2*pi*Omega*t; FiOmegaInt=interp1(t,FiOmega,t_PmfPhD); %faza la timpii caderilor...! |

PhaseDiff

| 1 | function [rap]=PhaseDiff(t_PmfPhD,FiPM,FiOmegaInt) |
| --- | --- |
| 2 |  |
| 3 | %pentru variatii liniare ale fazelor |
| 4 | %--------------------------------------verificarea formulei %Fi_EOM-n/m*Fi_Pm=const -> d_Fi_EOM/d_Fi_Pm=n/m |
| 5 |  |
| 6 | [pOm]=polyfit(t_PmfPhD,FiOmegaInt,1); |
| 7 | [pPM]=polyfit(t_PmfPhD,FiPM,1); |
| 8 | b1=pOm(1);b2=pPM(1); |
| 9 | [n,m] = rat(pOm(1)/pPM(1),0.1); %raportul tangentelor dreptelor de fitare liniare a fazelor... |
| 10 | %rats(pOm(1)/pPM(1)); |
| 11 | rap=n/m; %din raportul tangentelor fitarilor cu drepte...! el nu depinde de Zero...! |
| 12 | % n; |
| 13 | % m; |
| 14 |  |
| 15 | aO=pOm(2);bO=pOm(1); |
| 16 | aP=pPM(2);bP=pPM(1); |
| 17 | rap==bO/bP |
| 18 | figure;plot(t_PmfPhD, t_PmfPhD*pPM(1)+pPM(2), t_PmfPhD, t_PmfPhD*pOm(1)+pOm(2) ) |
| 19 | figure;plot(t_PmfPhD, rap*(t_PmfPhD*pPM(1)+pPM(2)),'r', t_PmfPhD, t_PmfPhD*pOm(1)+pOm(2),'g' ) |
| 20 | figure;plot(t_PmfPhD,FiPM,'r',t_PmfPhD,FiOmegaInt,'g') %fazele EOM si PM |
| 21 | figure;plot(t_PmfPhD, rap*(FiPM),'r', t_PmfPhD, FiOmegaInt,'g' ) |
| 22 | figure;plot(t_PmfPhD, n*FiPM,'r', t_PmfPhD, m*FiOmegaInt,'g' ) |
| 23 | figure;plot(t_PmfPhD, rap*(FiPM)- FiOmegaInt );title('rap*P-O') |
| 24 | figure;plot(t_PmfPhD, m*FiOmegaInt-n*FiPM -mean(m*FiOmegaInt-n*FiPM) ) |
| 25 |  |
| 26 | %calculam diferenta dintre Dif_faze si fitarea liniara a acesteia |
| 27 | Dif_faze_Zero=FiOmegaInt-FiPM; |
| 28 | Dif_faze_Zero=FiPM-FiOmegaInt; |
| 29 | figure;plot(t_PmfPhD,Dif_faze_Zero) |
| 30 | [pDif_faza]=polyfit(t_PmfPhD,Dif_faze_Zero,1); %drepta de fitare a Dif_faze |
| 31 | Dif_f=polyval(pDif_faza,t_PmfPhD); %diferenta de faza fitata |
| 32 | plot(t_PmfPhD,Dif_faze,t_PmfPhD,Dif_f) |
| 33 | figure;plot(t_PmfPhD,(Dif_faze_Zero-Dif_f));title('Graficul diferentei dintre (FiOmegaInt-FiPM) si fitarea ei...') |

RapFreq

| 1 | function [r_frq,r_faze]=RapFreq(t_PmfPhD,FiPM,FiOmegaInt) |
| --- | --- |
| 2 |  |
| 3 | NN=size(t_PmfPhD,1); |
| 4 |  |
| 5 | %cu raportul frecventelor |
| 6 | %------------------------------------------------------raportul frecventelor (in momentele t_PmfPhD) |
| 7 | FrqOmegaInt=diff(FiOmegaInt)./diff(t_PmfPhD); %calculul frecventei caderilor (are dimensiune < 1 unitate) |
| 8 | FrqPM=diff(FiPM)./diff(t_PmfPhD); %calculul frecventei modulatorului |
| 9 | r_frq=FrqOmegaInt./FrqPM; %raportul frecventelor instantanene la t_PmfPhD = m/n! |
| 10 | r_frq=[r_frq; r_frq(NN-1)]; %refac dimensiunea NN dubland ultima valoare |
| 11 | %ttt=cumsum(diff(t_PmfPhD)); |
| 12 | %figure;plot(t_PmfPhD,r_frq);title('R\Omega_{\it12}') |
| 13 |  |
| 14 | %cu raportul fazelor |
| 15 | r_faze=FiOmegaInt./FiPM; |
| 16 |  |
| 17 | figure;plot(t_PmfPhD,r_faze);title('R\phi_{\it12}') |

StatHist

| 1 | function [sigma_HIST,xhist,Pn1]=StatHist(r_frq,r_faze) |
| --- | --- |
| 2 | %global X NN Xii pdf_H sigma_HIST Smax S1 nxh n1 |
| 3 |  |
| 4 | %------cu histograma |
| 5 | %X=r_frq; |
| 6 | X=r_faze; |
| 7 |  |
| 8 | figure;plot(sort(X),'.') |
| 9 |  |
| 10 | NN=size(X,1); |
| 11 | NrIntervale=10; %NN/10; |
| 12 | [n,Xii] = hist(X,NrIntervale); |
| 13 | %sum(n)-NN==0 |
| 14 | pdf_H=n/NN+1e-90; |
| 15 | %figure;hist(X,NrIntervale); title('Histograma') |
| 16 |  |
| 17 | figure;plot(Xii,pdf_H);title('Histograma') |
| 18 | hist(X,NrIntervale) |
| 19 |  |
| 20 | xhist=0.4:0.25:3.4; % 13 components->12 bins |
| 21 | nxh=size(xhist,2)-1; % 12 bins |
| 22 | Smax=-log10(1/nxh); |
| 23 | n1=histc(X/1E-8,xhist); % n1=distribution vector of elements in bins |
| 24 | Pn1=n1/sum(n1); % normalize for plotting purposes only |
| 25 | n1norm=nonzeros(n1)/sum(n1); % normalize to the number of total elements and discard the zeroes |
| 26 | S1=-sum(n1norm.*log10(n1norm)); |
| 27 | sigma_HIST=(Smax-S1)/Smax |
| 28 |  |
| 29 | figure;bar(xhist,Pn1,'width',1); axis([0.5 3.3 0 0.82]); |
| 30 | h = findobj(gca,'Type','patch');set(h,'FaceColor',[0.4 0.4 0.4],'EdgeColor','k'); |
| 31 | xlabel('Time (\times 10^{-8} s)','fontsize',17);ylabel('Probability density','fontsize',17); |
| 32 | set(gca,'fontsize',16,'XColor','black','YColor','black');text(3.1,0.7,'a)','fontsize',20) |
| 33 |  |
| 34 | Ent_HIST=-sum(pdf_H.*log(pdf_H)); E_M_HIST=-log(1/size(pdf_H,2)); |
| 35 | sigma_HIST=(E_M_HIST-Ent_HIST)/E_M_HIST; |
| 36 |  |
| 37 | %---------------------------------- |
| 38 | din_StatHist=1 |
| 39 | sigma_HIST |

A1.4 Programe de afisare a datelor

SeriaTemporala

| 1 | clear;clc; |
| --- | --- |
| 2 | load I=0.015!A=0!Om=0!curent.mat; |
| 3 | %load I=0.015!A=1!Om=1970000000!eom.mat; |
| 4 |  |
| 5 | T0=0e-7; T1=1e-7; |
| 6 | [C,N0] = max(diff(sign(t-T0))); %N0 numarul pentru care timpul din simulare depaseste valoarea T=1e-7... |
| 7 | [C,N1] = max(diff(sign(t-T1))); |
| 8 | t=t(N0:N1); Pmf=Pmf(N0:N1); Pm=Pm(N0:N1); |
| 9 |  |
| 10 | %I=1.5e-3*(1+0.1*sin(2*pi*1.97e9*t)); |
| 11 |  |
| 12 | %------------------------graficul seriei temporale |
| 13 | plot(t*1e7,Pm*1e3,'g',t*1e7,Pmf*1e3,'k', 'LineWidth',2); axis([0 1 0 2.1]) |
| 14 | %title('LFF','fontsize',18); |
| 15 | xlabel('Time (\times 10^{-7} s)','fontsize',17); ylabel('I (\times 10^{-4} W)','fontsize',17); |
| 16 | set(gca,'fontsize',16,'XColor','black','YColor','black'); |
| 17 | legend('I','I_{filtered}',2); |

CoparareSeriiTemporale

| 1 | %------------------- |
| --- | --- |
| 2 | load I=0.015!A=0!Om=0!curent.mat; OmegaFazaI=[0 0]; |
| 3 | [t_PmfPhD,FiPM,FiOmegaInt,r_frq,sigma_HIST,xhist,Pn1]=CalculeazaDate(t,Pmf,OmegaFazaI(2)); |
| 4 | [C,N0] = max(diff(sign(t-0))); [C,N1] = max(diff(sign(t-0.6e-6))); |
| 5 | t1=t(N0:N1); P1=Pmf(N0:N1); |
| 6 | x1=xhist; H1=Pn1; |
| 7 | clear t_PmfPhD FiPM FiOmegaInt r_frq sigma_HIST xhist Pn1) |
| 8 |  |
| 9 | %------------------- |
| 10 | load I=0.015!A=1!Om=1970000000!eom.mat; OmegaFazaI=[0 1.97e9]; |
| 11 | [t_PmfPhD,FiPM,FiOmegaInt,r_frq,sigma_HIST,xhist,Pn1]=CalculeazaDate(t,Pmf,OmegaFazaI(2)); |
| 12 | [C,N0] = max(diff(sign(t-0))); [C,N1] = max(diff(sign(t-0.6e-6))); |
| 13 | t2=t(N0:N1); P2=Pmf(N0:N1); |
| 14 | x2=xhist; H2=Pn1; |
| 15 | clear t_PmfPhD FiPM FiOmegaInt r_frq sigma_HIST xhist Pn1) |
| 16 |  |
| 17 | %I2=0.015*(1+1/10*sin(2*pi*1.97e9*t2)); |
| 18 |  |
| 19 | %------------------- |
| 20 | load I=0.015!A=0.1!Om=1970000000!curent.mat; OmegaFazaI=[0 1.97e9]; |
| 21 | [t_PmfPhD,FiPM,FiOmegaInt,r_frq,sigma_HIST,xhist,Pn1]=CalculeazaDate(t,Pmf,OmegaFazaI(2)); |
| 22 | [C,N0] = max(diff(sign(t-0))); [C,N1] = max(diff(sign(t-0.6e-6))); |
| 23 | t3=t(N0:N1); P3=Pmf(N0:N1); |
| 24 | x3=xhist; H3=Pn1; |
| 25 | clear t_PmfPhD FiPM FiOmegaInt r_frq sigma_HIST xhist Pn1) |
| 26 |  |
| 27 | figure; |
| 28 | subplot(3,1,1);plot(t1*1e7,1e4*P1); axis([0 6 0 3]); text(5.5,2.5,'a)','fontsize',20); set(gca,'fontsize',16,'XColor','black','YColor','black'); |
| 29 | subplot(3,1,2);plot(t2*1e7,1e4*P2); axis([0 6 0 3]); text(5.5,2.5,'b)','fontsize',20); set(gca,'fontsize',16,'XColor','black','YColor','black'); |
| 30 | ylabel('I (\times 10^{-4} W)','fontsize',17); |
| 31 | %hold on; plot(t2,I2*1e2,'r');hold off |
| 32 | subplot(3,1,3);plot(t3*1e7,1e4*P3); axis([0 6 0 3]); text(5.5,2.5,'c)','fontsize',20); set(gca,'fontsize',16,'XColor','black','YColor','black'); |
| 33 | xlabel('Time (\times 10^{-7} s)','fontsize',17); |
| 34 |  |
| 35 | %ylabel('I (\times 10^{-4} W)','fontsize',17); |
| 36 |  |
| 37 | figure;title('Probability density','fontsize',18); |
| 38 | subplot(3,1,1);bar(x1,H1,'width',1); axis([0.5 3.3 0 0.82]); text(3.1,0.7,'a)','fontsize',20); set(gca,'fontsize',16,'XColor','black','YColor','black'); |
| 39 | subplot(3,1,2);bar(x2,H2,'width',1); axis([0.5 3.3 0 0.82]); text(3.1,0.7,'b)','fontsize',20); set(gca,'fontsize',16,'XColor','black','YColor','black'); |
| 40 | ylabel('Probability density','fontsize',17); |
| 41 | subplot(3,1,3);bar(x3,H3,'width',1); axis([0.5 3.3 0 0.82]); |
| 42 | xlabel('Time (\times 10^{-8} s)','fontsize',17); text(3.1,0.7,'c)','fontsize',20); set(gca,'fontsize',16,'XColor','black','YColor','black'); |
| 43 | %h = findobj(gca,'Type','patch');set(h,'FaceColor',[0.4 0.4 0.4],'EdgeColor','k'); |

AfisareRsiS

| 1 | load I=0.015!A=1!Om=1970000000!eom.mat; OmegaFazaI=[0 1.97e9]; |
| --- | --- |
| 2 | [t_PmfPhD,FiPM,FiOmegaInt,r_frq,sigma_HIST,xhist,Pn1]=CalculeazaDate(t,Pmf,OmegaFazaI(2)); |
| 3 | t2=t_PmfPhD; FL2=FiPM; FA2=FiOmegaInt; r2=r_frq; s2=sigma_HIST; |
| 4 | clear t_PmfPhD FiPM FiOmegaInt r_frq sigma_HIST xhist Pn1) |
| 5 |  |
| 6 | %3==I |
| 7 | load I=0.015!A=0.1!Om=1970000000!curent.mat; OmegaFazaI=[0 1.97e9]; |
| 8 | [t_PmfPhD,FiPM,FiOmegaInt,r_frq,sigma_HIST,xhist,Pn1]=CalculeazaDate(t,Pmf,OmegaFazaI(2)); |
| 9 | t3=t_PmfPhD; FL3=FiPM; FA3=FiOmegaInt; r3=r_frq; s3=sigma_HIST; |
| 10 | clear t_PmfPhD FiPM FiOmegaInt r_frq sigma_HIST xhist Pn1) |
| 11 |  |
| 12 | rr2=FA2./FL2; |
| 13 | rr3=FA3./FL3; |
| 14 | t2=t2*1e6; |
| 15 | t3=t3*1e6; |
| 16 | figure;hold on |
| 17 |  |
| 18 | plot(t2,FL2,'k--','LineWidth',2); |
| 19 | plot(t3,FL3,'k:','LineWidth',2); |
| 20 | plot(t2,rr2*10,'ks','MarkerSize',5) |
| 21 | plot(t3,rr3*10,'k.') |
| 22 | plot(t2,FA2/20,'k','LineWidth',4); |
| 23 |  |
| 24 | xlabel('Time (\times 10^{-6}s)','fontsize',17); |
| 25 | ylabel('{\Phi_L}^{eom}, {\Phi_L}^{current}, r^{eom}, r^{current}, \Phi_M','fontsize',18); |
| 26 | legend('{\Phi_L}^{eom}','{\Phi_L}^{current}','r^{eom}*10','r^{current}*10','\Phi_M/20',5,4); |
| 27 | set(gca,'fontsize',16,'XColor','black','YColor','black'); |

AfisareRsiS3D

| 1 | n=48; %Numarul de linii din seriile cu aceasi Amplitudine! domeniul de variatie alui kk! |
| --- | --- |
| 2 | %-------------------------------------------------- |
| 3 | load DDD_mat.mat; X=DDD; |
| 4 |  |
| 5 | f=X(1:n,1)/1e9; |
| 6 | a=X([1:n:size(X,1)-1],3); |
| 7 | %-------------------------------------------------- |
| 8 | [F,A]=meshgrid(f,a); |
| 9 | for kk=0:size(X,1)/n-1, for k=1:n |
| 10 | S(kk+1,k)=X(k+n*kk,2); |
| 11 | %SS=floor(S+prag); |
| 12 | R(kk+1,k)=X(k+n*kk,4); |
| 13 | end, end |
| 14 |  |
| 15 | nn=4; |
| 16 | ff=f(nn:end); |
| 17 | SS=S(1:end,nn:end); |
| 18 | RR=R(1:end,nn:end); |
| 19 |  |
| 20 | %-------------------------------------------pentru Graficele 3D |
| 21 | %figure;mesh(S,'XData',f,'YData',a);%colormap(gray); |
| 22 | figure;surf(ff,a,SS);colormap(gray);%title('\sigma','FontSize',22,'FontWeight','Bold') |
| 23 | xlabel('\Omega (GHz)','FontSize',12,'FontWeight','Bold');ylabel('A','FontSize',12,'FontWeight','Bold');zlabel('\sigma','FontSize',16,'FontWeight','Bold') |
| 24 |  |
| 25 | figure;surf(ff,a,RR);colormap(gray);%title('\sigma','FontSize',22,'FontWeight','Bold') |
| 26 | xlabel('\Omega (GHz)','FontSize',12,'FontWeight','Bold');ylabel('A','FontSize',12,'FontWeight','Bold');zlabel('r','FontSize',16,'FontWeight','Bold') |
| 27 |  |
| 28 | %----------------------------------------pentru graficele 2D |
| 29 | NrAmplit0=434; NrAmplit1=NrAmplit0+n-1; |
| 30 |  |
| 31 | SS=X(NrAmplit0:NrAmplit1,2); %X(:,1)==frecventele X(:,2)==sigma X(:,1)==A X(:,1)==r |
| 32 | RR=X(NrAmplit0:NrAmplit1,4); |
| 33 |  |
| 34 | figure; |
| 35 | plot(f,SS,'g-', 'LineWidth' ,4); hold on |
| 36 | xlabel('\Omega (GHz)','FontSize',17,'FontWeight','Bold');ylabel('\sigma','FontSize',17,'FontWeight','Bold');%title('\sigma','FontSize',22,'FontWeight','Bold') |
| 37 | set(gca,'fontsize',16,'XColor','black','YColor','black'); |
| 38 |  |
| 39 | plot(f,RR/100,'--rs', 'LineWidth' ,2, 'MarkerSize', 9) |
| 40 | xlabel('\Omega (GHz)','FontSize',17,'FontWeight','Bold');ylabel('r','FontSize',17,'FontWeight','Bold');%title('\sigma','FontSize',22,'FontWeight','Bold') |
| 41 | legend('\sigma','r/100',2); |

SpatiulFazelor

| 1 | load date_00; %tau=1e-9; |
| --- | --- |
| 2 |  |
| 3 | %scapam de tranzitia initiala |
| 4 | [C,N0] = max(diff(sign(t-1e-7))); %N0 numarul pentru care timpul din simulare depaseste valoarea T=1e-7... |
| 5 | [C,N1] = max(diff(sign(t-3e-7))); |
| 6 |  |
| 7 | t=t(N0:N1); |
| 8 | N=N(N0:N1); |
| 9 | E=Em(N0:N1); %valorile pe dinamica stabilizata! |
| 10 | PPmf=Pmf(N0:N1); |
| 11 | plot(t*1e7,PPmf*1e4) |
| 12 | axis([1 3 0 2.5]) |
| 13 | xlabel('Time (\times 10^{-7} s)','fontsize',17); ylabel('I (\times 10^{-4} W)','fontsize',17); |
| 14 | set(gca,'fontsize',16,'XColor','black','YColor','black'); |
| 15 |  |
| 16 | %---------------------------------------- |
| 17 | dt=min(diff(t)); %valaoarea cea mai mica de "samplare" |
| 18 | Nr=floor(tau/dt); %nr de pasi pentru a avea o intarziere de tau |
| 19 |  |
| 20 | tt=t(1):dt:t(end); |
| 21 | EE=interp1(t,E,tt); %interpolam la pasi egali dt... |
| 22 | %plot(t,Em,'g',tt,EE,'r') %verificam grafic echivalenta |
| 23 | N0=interp1(t,N,tt); |
| 24 | N0=N0/N0(1); |
| 25 |  |
| 26 | fi=unwrap(atan2(imag(EE),real(EE))); |
| 27 | ro=abs(EE); |
| 28 |  |
| 29 | N0N=N0(Nr+1:end); rro=ro(Nr+1:end); ffi=fi(Nr+1:end); %valorile spatiului fazelor de la Nr+1... end |
| 30 |  |
| 31 | dffi=fi(1:end-Nr)-fi(Nr+1:end); %valaoera... intarziata |
| 32 | dro=ro(1:end-Nr)-ro(Nr+1:end); |
| 33 |  |
| 34 | N0N0=N0N-0.79; |
| 35 |  |
| 36 | figure;plot3(dffi,dro,N0N0,'g.','MarkerSize',1) |
| 37 | hold on |
| 38 | plot3(dffi,ones(size(dro))*200,N0N0) |
| 39 | plot3(ones(size(dro))*25,dro,N0N0) |
| 40 | plot3(dffi,dro,ones(size(dro))*0.19) |
| 41 | axis([-150 25 -200 200 0.19 0.23]) |
| 42 | xlabel('\Psi(t)- \Psi(t-\tau)','FontSize',17,'FontWeight','Bold'); |
| 43 | ylabel('¦E(t)¦-¦E(t-\tau)¦','FontSize',17,'FontWeight','Bold') |
| 44 | zlabel('\DeltaN/N_0','FontSize',17,'FontWeight','Bold'); |
| 45 | set(gca,'fontsize',16,'XColor','black','YColor','black'); |